# How do I check if a variable is of a certain type (compare two types) in C
https://stackoverflow.com/questions/6280055/how-do-i-check-if-a-variable-is-of-a-certain-type-compare-two-types-in-c

Getting the type of a variable is, as of now, possible in C11 with the _Generic generic selection. It works at compile-time.
The syntaxis is a bit like switch. Here's a sample (from this answer):
#define typename(x) _Generic((x), \
        _Bool: "_Bool", unsigned char: "unsigned char", \
        char: "char", signed char: "signed char", \
    short int: "short int", unsigned short int: "unsigned short int", \
        int: "int", unsigned int: "unsigned int", \
     long int: "long int", unsigned long int: "unsigned long int", \
long long int: "long long int", unsigned long long int: "unsigned long long int", \
        float: "float", double: "double", \
  long double: "long double", char *: "pointer to char", \
       void *: "pointer to void", int *: "pointer to int", \
      default: "other")
To actually use it for compile-time manual type checking, you can define an enum with all of the types you expect, something like this:
enum t_typename {
    TYPENAME_BOOL,
    TYPENAME_UNSIGNED_CHAR,
    TYPENAME_CHAR,
    TYPENAME_SIGNED_CHAR,
    TYPENAME_SHORT_INT,
    TYPENAME_UNSIGNED_CHORT_INT,
    TYPENAME_INT,
    /* ... */
    TYPENAME_POINTER_TO_INT,
    TYPENAME_OTHER
};
And then use _Generic to match types to this enum:
#define typename(x) _Generic((x), \
        _Bool: TYPENAME_BOOL, unsigned char: TYPENAME_UNSIGNED_CHAR, \
        char: TYPENAME_CHAR, signed char: TYPENAME_SIGNED_CHAR, \
    short int: TYPENAME_SHORT_INT, unsigned short int: TYPENAME_UNSIGNED_SHORT_INT, \
        int: TYPENAME_INT, \
    /* ... */ \
        int *: TYPENAME_POINTER_TO_INT, \
      default: TYPENAME_OTHER)

# Global Variable in C are Static or Not
If you do not specify a storage class (that is, the extern or static keywords), then by default global variables have external linkage. From the C99 standard:
§6.2.2 Linkages of identifiers
1) If the declaration of a file scope identifier for an object or a function contains the storage-class specifier static, the identifier has internal linkage.
2) If the declaration of an identifier for a function has no storage-class specifier, its linkage is determined exactly as if it were declared with the storage-class specifier extern. If the declaration of an identifier for an object has file scope and no storage-class specifier, its linkage is external.
So even if you don't specify the extern keyword, globals can still be accessed by other source files (so-called translation units), because they can still have an extern declaration for the same variable. If you use the static keyword to specify internal linkage, then even in the presence of an extern declaration for the same variable name in another source file, it will refer to a different variable.